UDO - Universal Device Objects
First Published:	2023-04-30
Publish Site:	github.com/nvitya/udo
Original Author:	Viktor Nagy
License Type	MIT (Open Source)
Actual Version, date:	1.0, 2023-04-30

Basics
The UDO is a simple, universal, binary master-slave data exchange system.
The slave data selected by a 16-bit address and an optional 32-bit offset.
The offset is a data byte offset by default, but the implementation can vary from object to object, like using as a sub-object identifier.

Targeted communication mediums:
- UART serial communication
- USB (serial communication emulation)
- IP (UDP)

Common (Mandatory) Device Objects

Obj. / (hex)	Type	R/W	Function
Test Objects, Generic device Information (Mandatory)
0000	u32	R	Communication Test Object, fix 0x66CCAA55
0001	u32	R	Maximal data (payload) length: 64 - 1024. / The smaller devices might not support the maximal 1024 byte payload.
0002	blob	RW	Blob Test Object, data size = 262144 bytes / It returns 16384 * 32-bit integer numbers in ascending order beginning with 0. / The OFFSET handled as byte offset here. / Its main purpose to test the device large data transfers. / By writing an error code will be responded if the written data does not corresponds the proper incrementing numbers.
0003	str[32]	R	Device SW (Firmware) Identification / Useful for pre-configuration check.
0004	u32	R	Device SW version
Device Generic Setup (Mandatory)
0010	u8	RW	Configuration Status and Control / Read and Write: / 0 = CONFIG mode: outputs should be safe, configuration objects are writeable / 1 = RUN mode: outputs activated, configuration objects are read only / Write only: / 2 = restart device (keeps the actual CONFIG/RUN status) / Writing value 1 saves the configuration into the internal non-volatile storage. When the device starts loads the configuration and goes into RUN mode then. / Writing value 0 does not clears the previous configuration, and when the device restarts it might start in RUN mode again. / Beware, that too frequent configuration save might wear out the Flash memory used for storage in the devices. / Generic device in the manufactured state or without valid configuration must be CONFIG mode.
0011	str[32]	RW	Device ID / Used as the USB Device ID too. / Recommended to assign a unique ID for different configurations and / or different pieces.
0012	u16	RW	USB Vendor ID
0013	u16	RW	USB Product ID
0014	str[32]	RW	Manufacturer Name
0015	str[32]	RW	Serial Number / Used as the USB Device Serial number too.

Serial Request Format
Bytes	Segment ID	Description
1	SYNC	sync byte, always = 0x55
1	OFFSLEN, / MLEN, / LEN, / RW	Read/Write and length information / bit0..1: OFFSLEN: offset length 0=0, 1=1, 2=2, 3=4 / bit2..3: MLEN: metada length, 0=0, 1=1 byte, 2=2, 3=4 / bit4..6: LEN: read or write length, if LEN = 7 then EXTLEN follows / 0=0, 1=1, 2=2, 3=4, 4=8, 5=16, 6=INVALID, 7=EXTLEN / bit7: RW: 0 = read, 1=write
0 | 2	EXTLEN	16-bit extended length, present only if LEN = 7
2	INDEX	16-bit Object Index
0 - 4	OFFSET	0 - 32 bit offset, if OFFSLEN > 0
0 - 4	METADATA	Optional metadata,present only if MLEN > 0 / Can be useful for extra request parameters
0 - 1024	WDATA	Write data. Present only if RW=1, length determined by LEN or EXTLEN (when LEN = 15).
1	CRC	The CRC calculated for all the previous bytes (including the SYNC byte). / The CRC8 generator polinom is 0x07.

Serial Response Format
Bytes	Segment ID	Description
1	SYNC	sync byte, always = 0x55
1	OFFSLEN, / MLEN, / LEN, / RW	Read/Write and length information / bit0..1: OFFSLEN: offset length 0=0, 1=1, 2=2, 3=4 / bit2..3: MLEN: metada length, 0=0, 1=1 byte, 2=2, 3=4 / bit4..6: LEN: read or write length, if LEN = 7 then EXTLEN follows / 0=0, 1=1, 2=2, 3=4, 4=8, 5=16, 6=ERROR CODE, 7=EXTLEN / bit7: RW: 0 = read, 1=write
0 | 2	EXTLEN	16-bit extended length, present only if LEN = 7
2	INDEX	16-bit Object Index
0 - 4	OFFSET	0 - 32 bit offset (mirrored from the request), if OFFSLEN > 0
0 - 4	METADATA	Optional metadata (mirrorred from request), present only if MLEN > 0.
0 | 2	ECODE	16-bit error code, present only if ERR = 1
0 - 1024	RDATA	Read data. Present only if RW=0 (read), and ERR = 0. / Length determined by LEN or EXTLEN (when LEN = 15).
1	CRC	The CRC calculated for all the previous bytes (including the SYNC byte). / The CRC8 with generator polinom is 0x07.

IP Request Format
Bytes	Segment ID	Description
4	RQID	Request ID
2	LEN, / MLEN, / RW	Data Length + CMD / bit0..10: LEN (0..1024), LEN > 1024 = INVALID / bit11..12: reserved / bit13..14: MLEN: metada length, 0=0, 1=1 byte, 2=2, 3=4 / bit15: RW: 0 = read, 1 = write
2	INDEX	16-bit Object Index
4	OFFSET	0 - 32 bit offset
4	METADATA	Metadata, meaningful only when MLEN > 0 / Can be useful for extra request parameters / 4 bytes will be used when MLEN=1, or MLEN=2
0 - 1024	WDATA	Write data. Present only if RW=1, length determined by LEN

IP Response Format
Bytes	Segment ID	Description
4	RQID	Request ID
2	LEN, / MLEN, / RW	Data Length + CMD / bit0..10: LEN: if 0..1024 response data length, 0x7FF = ERROR CODE / bit11..12: reserved / bit13..14: MLEN: metada length, 0=0, 1=1 byte, 2=2, 3=4 / bit15: RW: 0 = read, 1 = write
2	INDEX	16-bit Object Index
4	OFFSET	0 - 32 bit offset
4	METADATA	Metadata, meaningful only when MLEN > 0 / Can be useful for extra request parameters / 4 bytes will be used when MLEN=1, or MLEN=2
0 | 2	ECODE	16-bit error code, present only if LEN=0x7FF
0 - 1024	RDATA	Write data. Present only if RW=1, length determined by LEN (if LEN <= 1024)

CAN
The CAN compatibility is to be defined.
Ideally it should work trough CANopen SDO requests, but this way it is impossible to send properly the read length, 32-bit offset or metadata.